## Slide 1
Simplifying complex Embedded Development processes with mbeddr
JC-M, 29.10.2013

## Slide 2
Motivation.
Automotive specific extensions.
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 3
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 4
Context.
What is mbeddr?
An extensible set of integrated languages
for embedded software engineering.
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 5
Context.
What is mbeddr?
And an IDE for everything.
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 6
Context.
What is mbeddr?
Open Source
Eclipse Public License
http://mbeddr.com
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 7
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 8
Context.
What is MPS?
Language Workbench.
Projectional Editing
Textual/Symbolic/Tabular/(soon Graphical)
Multiple projections for the same language
Modular language development, extension and embedding
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 9
Context.
What is MPS?
Support for language aspects such as type system, scopes, code completion, find usages, dataflow
Template-based approach for transformation and code generation with IDE support for target language in templates
Support for building extensible debuggers
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 10
Context.
What is MPS?
Open Source
Apache 2.0
http://jetbrains.com/mps
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 11
MPS.
SUPported notations: Text
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 12
MPS.
SUPported notations: tables
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 13
MPS.
SUPported notations: Math
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 14
MPS.
SUPported notations: diagrams
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 15
MPS.
Let’s see how it works.
DEMO
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 16
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 17
Virtual Function Bus (VFB)
AUTOSAR.
A Brief introduction.
Software
Component 1
Software
Component 2
Software
Component 3
ECU 1
Software
Component 1
Software
Component 2
RTE
Basic Software
ECU 2
Software
Component 3
RTE
Basic Software
Notes: AUTOSAR VFB View and AUTOSAR System View

## Slide 18
AUTOSAR.
A Brief introduction.
Software
Component 1
AUTOSAR Runtime Environment (RTE)
Basic Software
Software
Component 1
Software
Component n
ECU Hardware
AUTOSAR
Interface
AUTOSAR
Interface
AUTOSAR
Interface
AUTOSAR
Software
Notes: AUTOSAR ECU View: RTE as VFB implementation

## Slide 19
Components |  | 
Runnable Entities |  | 
Interfaces: |  | 
- Sender / Receiver |  | 
- Client / Server |  | 
- Mode Switch |  | 
Parameter |  | 
Data Types: |  | 
Modes |  | 
- Mode Groups |  | 
Event Trigger: |  | 
Timing |  | 
Server Call |  | 
Mode Switch |  | 
AUTOSAR in mbeddr?
The Challenge.
Notes: Which language concepts were missing in the mbeddr core language and what was already covered?

## Slide 20
AUTOSAR in mbeddr.
The solution.
Introduction of AUTOSAR specific language extensions:
Parameter Interface
Mode Groups
Mode Switch Interfaces
Mode Triggers for Runnables
Notes: - AUTOSAR specific language concepts added by extending the existing component language
1st step is done: component language is powerful enough to user necessary concepts from the software component template
Next step: closer look on the AUTOSAR methodology

## Slide 21
AUTOSAR.
Methodology.
Specify Software Component
Software Component description (XML)
Functional Specification
Implement Software Component
Software Component description (XML)
Rte_Swc.h
Rte_Type.h
Rte.h
SWC.c
Generate Component Header
Software Component description (XML)
Rte_Swc.h
Rte_Type.h
Rte.h
Compile Software Component
SWC.c
Rte_Swc.h
Rte_Type.h
Rte.h
SWC.o
Notes: Focus on software component implementation (not integration):
Each step requires a different tool
subsequent steps depend on artifacts from previous steps
artifacts are mainly „handmade“ and only partly generated
very long feedback loops

## Slide 22
AUTOSAR.
Methodology.
Generate Component Header
Specify Software Component
Implement Software Component
Compile Software Component
Notes: very long feedback loops

## Slide 23
AUTOSAR methodology.
Simplification.
1. Simplify
Software Component Specification

## Slide 24
AUTOSAR methodology.
Software component Specification.
VS.
Notes: Component specification in AUTOSAR XML vs. Using the component language in mbeddr:
Ugly XML
Special authoring tool is needed
BUT: AUTOSAR XML is needed as an exchange format
 Why shouldn‘t we use just the mbeddr component language?

## Slide 25
AUTOSAR methodology.
SWC Description with mbeddr.
Model Transformation
AUTOSAR XML Description
(http://www.artop.org)
Notes: Tool extension: Using Artop for AUTOSAR serialization

## Slide 26
AUTOSAR methodology.
Simplification.
2. Simplify
Software Component Implementation

## Slide 27
AUTOSAR methodology.
Simplification.
Do we really need to know which middleware is used?
Notes: Focus on platform independent implementation
Generator should take care about underlying platform
 Solution: Extend the mbeddr generator

## Slide 28
AUTOSAR IMPLEMENTATION.
State of the ART.
Swc
S/R Interface
uint8 State
MyRunnable
#include "Rte_Swc.h"
void MyRunnable()
{
uint8 state;
Rte_Read_RPort_State(&state);
}
Swc.c
Notes: Simple example of a component accessing a data element of a s/r interface: plain C
AUTOSAR Specific function call
RTE specification must be well known by software developer

## Slide 29
AUTOSAR IMPLEMENTATION.
The mbeddr way.
Swc
S/R Interface
uint8 State
MyRunnable
Notes: Simple example of a component accessing a data element of a s/r interface: mbeddr C
The only platform specific information needed is the @AUTOSAR port annotation
No special AUTOSAR knowledge needed
BUT: We still need the RTE header files to compile the generated code

## Slide 30
AUTOSAR methodology.
Software component Header Generation.
MBEDDR CORE
generate
MyModule.c
MyModule.h
MBEDDR CORE +
AUTOSAR
EXTENSIONS
AUTOSAR
RELATED
MyModule.c
MyModule.h
Rte_Type.h
Rte_Swc.h
Rte_Swc_Type.h
generate
Notes: With an AUTOSAR specific extension of the mbeddr generator the necessary header files are generated from the mbeddr implementation

## Slide 31
AUTOSAR methodology.
Using mbeddr.
Implement Software Component
Rte_Swc.h
Rte_Type.h
Rte.h
Software Component description (XML)
SWC.c
SWC.o
Functional Specification
Notes: The software developer can focus on implementation (taking into account the external = AUTOSAR interfaces)
all artifacts are generated in one step and with one tool
Maybe some comments, that the described scenario is very idealistic (one person doing all steps, mbeddr is the master, …)

## Slide 32
MPS.
Mbeddr + autosar
DEMO
Notes: Using mbbedr in the automotive domain  AUTOSAR as a main requirement

## Slide 33
Thank you!